STATE OF NEW YORK

DEPARTMENT OF TAXATION AND FINANCE

Office of Budget & Management Analysis

Bureau of Fiscal Services

Building 9, Room 234

W.A. Harriman Campus

Albany, NY  12227

Patricia Mitchell, Chief Financial Officer

Eric Mostert, Assistant Director, Budget & Accounting Services

Catherine Golden, Assistant Director, Procurement

May 25, 2011

Amendment 4 to RFP #10-34 – High Speed Single Pass Document and Remittance Scanner Solution

To All Potential Bidders:

The Department is amending the High Speed Single Pass Document and Remittance Scanner Solution RFP #10-34 for the following:

- Schedule of Events;

- Functional Requirements; and

- Attachment D – High Speed Single Pass Document and Remittance Scanner Solution Response Form.

# Replacement pages are attached to this notice with deletions shown in strikethrough and additions shown in red.  All other requirements remain as indicated in the RFP.

# Schedule of Events

| Issuance of RFP | March 1, 2011 |
| --- | --- |
| Deadline for filing Offerer Understanding of, and compliance with, Procurement Lobbying Guidelines | March 15, 2011 by 2 pm EST |
| Deadline for Submission of Questions | March 15, 2011 by 2 pm EST |
| Department Response to Bidder Questions | March 22, 2011 |
| Deadline for Submission of Notification of Intent to Bid | March 29, 2011 June 10, 2011 |
| Proposals Due | April 15, 2011 by 2 pm EST June 27, 2011 |
| Notification of Intent to Award | May 13, 2011 July 20, 2011 |
| Deadline for Contract Signature | June 13, 2011 August 19, 2011 |
| Tentative Installation of first delivery | August 15, 2011 September 20, 2011 |

There were numerous factors analyzed as part of this study including:  electronic filing (e-File) projections and the effect on paper filings; throughput; technology (various solutions were considered); staffing (development and operational); space and facility needs; equipment; costs and savings; and risks and benefits.  As the Department moves towards maximizing its e-file initiative, there are a number of factors that do not make 100 percent e-file compliance practicable at this time (e.g. necessary authorizations, allocation of resources and software vendor support.)  Recognizing there will be residual paper for the foreseeable future, the Department plans to expand its existing RPC to bring in other large complex tax applications such as Personal Income Tax, Sales Tax, Miscellaneous Tax etc.  The size and scope of a tax processing program such as Corporation Tax requires a more robust processing system than the current RPC system.

Although the Department’s current focus is to process Corporation Tax returns utilizing the solution that the successful bidder provides as a result of this bid, the Department is continuing to consider residual paper associated with other tax types which may be processed utilizing the proposed solution.    The solution as a result of this bid must allow for the Department to process other various tax type documents where each type may have their own business rules; allow  for a solution that has the capability for future expansion and modification and allow for the solution to be configurable and/or compatible with any future solutions purchased during the first year of the contract to accommodate the expansion (i.e. if the winning Bidder proposes model # 12345 and then discontinues this model, the Department would like assurances that the future offering from the vendor will be compatible with the solution previously provided).  In acknowledgement of the possibility of other tax types being required to be processed through the RPC, the Department reserves the right to procure up to thirty percent (30%) additional single pass document and remittance scanner solutions within the first year of the contract, but cannot commit nor guarantee the future purchase of these additional scanner solutions.

Currently, there are eighty-three various types of Corporation Tax forms for Tax Year 2009 which include primary returns and associated attachments.   This program has two large processing peaks; the months of March and September.   In processing year 2009, 900,000 Corporation Tax paper filings were processed.  With the expansion of the Corporation Tax e-file program it is anticipated that the volume of paper forms will decrease significantly by the time this program is put into production.

It is estimated that 341,000 250,000 Corporation Tax paper filings will be processed in 2013.  It is further estimated that during the processing peak periods the volume will be 125,000 100,000 filings per month, with the average number of pages being eighteen; though several forms have just one page.

DTF’s RPC which currently processes Highway Use Tax and other smaller miscellaneous tax documents will be expanded to process Corporation Tax.  The Corporation Tax system will consist of four major components:

# Functional Requirements

Certain requirements are considered critical to successful project implementation.  These critical requirements are indicated as Mandatory.  The Bidders response will be evaluated to determine if it meets these mandatory critical requirements.  Therefore, Bidders must provide the Department with all the information requested to establish they meet the minimums identified in the mandatory requirements.  Failure to provide sufficient detail to the mandatory topics of this section will result in the Bidder being deemed non-responsive and removed from further consideration.  Bidder responses which meet those minimums will gain evaluation points in the scoring process to the extent the proposed solution exceeds what is required. The Bidder’s response to desirable requirements will be evaluated and scored.

## High Speed Single Pass Document and Remittance Scanner Solution

The DTF requires a high speed single pass document and remittance scanner solution that is capable of processing returns and remittances in a single pass for both a processing site and disaster recovery site.  The solution proposed must be inclusive of installation and set up in the Department’s processing and disaster recovery sites in the Albany, New York area.  The solution must also be inclusive of all hardware and software required to meet the specifications below.

Given the anticipated volume of returns and remittances received during a peak period of 177,200131,600 per day and that a processing day for peak periods is considered a 6 hour shift, the bidder must correctly size and configure the solution.  Listed below is an estimation of the processing needs for peak periods:

- 9,400 7,000  Returns daily

- 8,000 5,600 Remittances daily

- Average of 18 pages per return

- Total average pages and remittances per day 177,200 131,600

The following are mandatory requirements.  Any bid which cannot provide a solution that meets ALL of these mandatory requirements will be deemed non-responsive and removed from further consideration.  As mentioned above, Bidder responses will gain evaluation points in the scoring process to the extent the proposed solution exceeds what is required.:

- Scanner Solution must be capable of handling a wide range of shapes, sizes and colors.

- Scanner Solution must run on a Windows 7 platform and quad processing CPU’s.

- Scanner solution must include a CPU with a quad processor, a flat panel touch screen monitor and an integrated keypad.

- Scanner Solution must have the ability to interface with 3i Infotech (J&B) Transaction Maintenance Software.

- Scanner Solution must have the ability to change dpi within the job to use 300 dpi for documents and 200 dpi for checks or must be able to convert the checks from 300 dpi to 200 dpi.

- Scanner Solution must have the ability to provide a separate test environment.

- Scanner Solution must have the ability to establish operator security levels at the scanner level.

- Scanner Solution must have a mechanism to detect blank pages for elimination.

- Scanner Solution must support both Auto and Drop feed ability.

- Scanner Solution must have the ability to in line re-scan images.

- Scanner Solution must have a mechanism to detect size and thickness to reduce jamming.

- Scanner Solution must support form ID recognition by reading Courier 12 point font, 1D Barcode, 2 of 5 interleave and 2D Barcode, PDF-417.

- Scanner Solution must have the ability to read checks by MICR (magnetic ink character recognition) and/or E13B font.

- Scanner Solution must have the ability to use checks as transaction separators.

- Scanner Solution must have the ability to execute business rules in line when scanning.

- Scanner Solution must have the ability to support a configurable tracking number.

- Scanner Solution must have the ability to print the tracking number on the document being scanned, in a specific location defined by the Department.

- Scanner Solution must have the ability to sequentially assign a batch number (to be determined by the Department), without gaps, across multiple scanners.

- Scanner Solution must have the ability for customized batch ticket printing which allows for printing of both a customized full page and an envelope size batch cover sheet (identifying the tax type, processing date, received date, batch number, first and second sort levels, document count, current date and time, and scanner unit number) at the completion of each batch.

- Scanner Solution must have the ability to annotate in a specific location defined by the Department, the document locator number and any remittance amount applied to the document.

- Scanner Solution must have the ability to generate reports (statistical, throughput, jam rates, management tools, etc.)

- Scanner Solution must include a CPU with a quad processor, a flat panel touch screen monitor and an integrated keypad.  The CPU must have a separate electric connection with power backups.

- Scanner Solution must include a minimum of six (6) sort trays-stackers per unit and six (6) pockets (output sort bins) to segregate scanned documents.

- Scanner Solution must include an image enhancement tool.

The following are the desirable requirements.  Responses to Desirable requirements will be evaluated and scored.:

- The ability for auto-rotation of documents.

- The ability to print the tracking number on both front and back of the document being scanned.

- The ability to put the pages of each transaction in sequential page order regardless of the order scanned.

- The ability to run on a 110 electric line.

- The CPU should have a separate electric connection with power backups.

- The ability to compile all statistical information from a various number of scanners into one summary report.

- Scanner Solution that provides the ability to view and classify every image scanned in real time and color code each document type for easy verification on the scanner’s monitor.

- Scanner Solution that includes a motorized height table to allow for a diverse pool of operators.

- Six (6) sort trays – stackers per unit (organizational bins for pre-process work and supplies).

Installation will be in two sites in the Albany Area.  The primary site will be set up for daily processing.  The secondary site will be set up for disaster recovery.  The disaster recovery site should assume processing at 30% of the average daily numbers.

Response Requirement

The Bidder must complete Attachment D, High Speed Single Pass Document and Remittance Scanner Solution Response Form, identifying the following:

An explanation of why the Bidder is the best qualified to provide the High Speed Single Pass Document and Remittance Scanner Solution and demonstrate its qualification.

# Attachment D – High Speed Single Pass Document and Remittance Scanner Solution Response Form

This form is for the Functional Requirements as specified in Section III. A.

The Bidder must provide a narrative description detailing how the proposed solution meets each of the requirements of Section III. A.  The Bidder’s response must provide the Department with a clear description of how the proposed Solution, including the necessary Hardware and Software Components, meets each of the bulleted items below.  Failure to provide sufficient detail to the mandatory topics of this section will result in the Bidder being deemed non responsive and removed from further consideration.  Bidder responses which meet those minimums will gain evaluation points in the scoring process to the extent the proposed solution exceeds what is required.  The Bidder’s response to desirable requirements will be evaluated and scored.

The following are mandatory requirements.  Any bid which cannot provide a solution that meets ALL of these requirements will be deemed non-responsive and removed from further consideration.  As mentioned in Section III. A, Bidder responses will gain evaluation points in the scoring process to the extent the proposed solution exceeds what is required.:

- Scanner Solution must be capable of handling a wide range of shapes, sizes and colors.

- Scanner Solution must run on a Windows 7 platform and quad processing CPU’s.

- Scanner solution must include a CPU with a quad processor, a flat panel touch screen monitor and an integrated keypad.

- Scanner Solution must have the ability to interface with 3i Infotech (J&B) Transaction Maintenance Software.

- Scanner Solution must have the ability to change dpi within the job to use 300 dpi for documents and 200 dpi for checks or must be able to convert the checks from 300 dpi to 200 dpi.

- Scanner Solution must have the ability to provide a separate test environment.

- Scanner Solution must have the ability to establish operator security levels at the scanner level.

- Scanner Solution must have a mechanism to detect blank pages for elimination.

- Scanner Solution must support both Auto and Drop feed ability.

- Scanner Solution must have the ability to in line re-scan images.

- Scanner Solution must have a mechanism to detect size and thickness to reduce jamming.

- Scanner Solution must support form ID recognition by reading Courier 12 point font, 1D Barcode, 2 of 5 interleave and 2D Barcode, PDF-417.

- Scanner Solution must have the ability to read checks by MICR (magnetic ink character recognition) and/or E13B font.

- Scanner Solution must have the ability to use checks as transaction separators.

- Scanner Solution must have the ability to execute business rules in line when scanning.

- Scanner Solution must have the ability to support a configurable tracking number.

- Scanner Solution must have the ability to print the tracking number on the document being scanned, in a specific location defined by the Department.

- Scanner Solution must have the ability to sequentially assign a batch number (to be determined by the Department), without gaps, across multiple scanners.

- Scanner Solution must have the ability for customized batch ticket printing to allow for printing of both a customized full page and an envelope size batch cover sheet (identifying the tax type, processing date, received date, batch number, first and second sort levels, document count, current date and time, and scanner unit number) at the completion of each batch.

- Scanner Solution must have the ability to annotate, in a specific location defined by the Department, the Document locator number and any remittance amount applied to the document.

- Scanner Solution must have the ability to generate reports (statistical, throughput, jam rates, management tools, etc.)

- Scanner Solution must include a CPU with a quad processor, a flat panel touch screen monitor and an integrated keypad.  The CPU must have a separate electric connection with power backups.

- Scanner Solution must include a minimum of six (6) sort trays-stackers per unit and six (6) pockets (output sort bins) to segregate scanned documents.

- Scanner Solution must include an image enhancement tool.

The following are the desirable requirements.  Responses to Desirable requirements will be evaluated and scored.:

- The ability for auto-rotation of documents.

- The ability to print the tracking number on both front and back of the document being scanned.

- The ability to put the pages of each transaction in sequential page order regardless of the order scanned.

- The ability to run on a 110 electric line.

- The CPU should have a separate electric connection with power backups.

- The ability to compile all statistical information from a various number of scanners into one summary report.

- Scanner Solution that provides the ability to view and classify every image scanned in real time and color code each document type for easy verification on the scanner’s monitor.

- Scanner Solution that includes a motorized height table to allow for a diverse pool of operators.

- Six (6) sort trays – stackers per unit (organizational bins for pre-process work and supplies).

Installation will be in two sites in the Albany Area.  The primary site will be set up for daily processing.  The secondary site will be set up for disaster recovery.  The disaster recovery site should assume processing at 30% of the average daily numbers.

Bidder must include a explanation of why the Bidder is the best qualified to provide the High Speed Single Pass Document and Remittance Scanner Solution (expand as necessary):  
__________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________

The make and model of the High Speed Single Pass Document and Remittance Scanner Proposed:  _______________________________________________________________

Hourly throughput of scanner proposed:  ________________________________________

A complete narrative describing how the proposed solution meets each of the mandatory requirements and any of the desirable requirements.  This narrative should include all information deemed pertinent to the proposal including, but not limited to, hardware and software required including any limitations or restrictions, technical manuals, product brochures, dvd or web presentations, sample reports manual, a technical description of how the solution will interface with 3i Infotech (J & B) TMS Software, etc.:

__________________________________________________________________________

__________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________

Number of Scanners proposed to process average pages and remittances per day (131,600 177,200):

_______________________________________________________________________

Bidder affirms understanding that all software licenses are perpetual and software license agreements are negotiable to meet the terms and conditions of this RFP.

Yes       No

In addition, attach the owners manual of the scanner proposed and copies of all software licenses.

Bidder Name:  _______________________________________________

Title:  ______________________________________________________

Signature:  __________________________________________________